A TRUST REGION AGGRESSIVE SPACE MAPPING ALGORITHM

FOR EM OPTIMIZATION

M.H. Bakr, J.W. Bandler, R.M. Biernacki, S.H. Chen and K. Madsen

SOS-97-9-R

November 1997

( M.H. Bakr, J.W. Bandler, R.M. Biernacki, S.H. Chen and K. Madsen

No part of this document may be copied, translated, transcribed or entered in any form into any machine without written permission.  Address inquiries in this regard to Dr. J.W. Bandler.  Excerpts may be quoted for scholarly purposes with full acknowledgment of source.  This document may not be lent or circulated without this title page and its original cover.

A TRUST REGION AGGRESSIVE SPACE MAPPING ALGORITHM

FOR EM OPTIMIZATION

M.H. Bakr, J.W. Bandler, R.M. Biernacki, S.H. Chen and K. Madsen

Simulation Optimization Systems Research Laboratory

and Department of Electrical and Computer Engineering

McMaster University, Hamilton, Canada L8S 4L7

Tel  905 628 8228

Fax  905 628 8225

Email j.bandler@ieee.org

Abstract

A robust new algorithm for EM optimization of microwave circuits is presented.  The algorithm integrates a trust region methodology with the aggressive space mapping (ASM) concept.  The trust region ensures that each step taken results in improved alignment between the coarse and fine models needed to execute ASM.  A new automated multi-point parameter extraction process is implemented.  Waveguide transformer design, and EM optimization of a double-folded stub filter and of an HTS filter illustrate our new results.

SUMMARY

Introduction

A novel algorithm for aggressive space mapping (ASM) EM optimization [1] is introduced.  Space mapping aims at aligning two different simulation models:  a “coarse” model,  typically an empirical circuit simulation and a “fine” model, typically a full wave EM simulation.  The technique combines the accuracy of the fine model with the speed of the coarse model.

This work was supported in part by Optimization Systems Associates Inc. (before acquisition by HP EEsof) and in part by the Natural Sciences and Engineering Research Council of Canada under Grants OGP0007239 and OGP0042444 and through the Micronet Network of Centres of Excellence.  M.H. Bakr is funded by TRIO through a student internship.

K. Madsen is with the Institute of Mathematical Modeling, Technical University of Denmark, DK-2800 Lyngby, Denmark.

Parameter extraction is a crucial part of the technique.  In this step the parameters of the coarse model whose response matches the fine model response is obtained.  The extracted parameters may not be unique, causing the technique to fail to converge to the optimal design.

Recently, a multi-point parameter extraction concept was proposed [2] to enhance the uniqueness of the extraction step at the expense of an increased number of fine model simulations.  The selection of points was arbitrary,  not automated and no information about the mapping between the two spaces was taken into account.

Our proposed ASM algorithm automates the selection of fine model points used for the multi-point parameter extraction step.  An iterative approach utilizes all the fine model points simulated since the last successful iteration in the multi-point parameter extraction.  Also, the current approximation to the mapping between the two spaces is integrated into the parameter extraction step.

The step taken at each iteration is constrained by a suitable trust region [3].  The size of this trust region is modified according to the match between the actual reduction in the misalignment between the two spaces and the predicted reduction in the misalignment.  This ensures that the alignment between the two spaces is improved in each iteration.

The New Algorithm

At the ith iteration, the error vectordefines the difference between the vector of extracted coarse model parameters =and the optimal coarse model design in the “os” space.  Subscript “em” identifies the fine model space, P denotes the mapping function.  The mapping between the two models is established if this error vector is driven to zero.  So, the value can serve as a measure of the misalignment between the two spaces in the ith iteration.  The step taken in the ith iteration is given by

(1)

where  is an approximation to the Jacobian of the coarse model parameters with respect to the fine model parameters at the ith iteration.  The parameter ( is selected such that the step obtained satisfies , where (  is the size of the trust region.  This is done utilizing the iterative algorithm suggested in [3].  The candidate point for the next iteration is .  Single point parameter extraction is then applied at the point to get.  The point is accepted if it satisfies a success criterion related to a reduction in the norm of the vector. Then the matrix is updated using Broyden’s formula [4].  Otherwise, the validity of the extraction process leading toat the suggested point  is suspect.  The residual error  is then used to construct a candidate step from the point by using (1).  The new point is then added to the set of points employed for simultaneous parameter extraction: a new value for  is obtained by solving

,                                             (2)

simultaneously for all , where V is the set of fine model points used for multi-point parameter extraction.  Thus, the extracted vector of coarse model parameters is obtained by matching the responses of the two models at a number of points in the parameter space.  Also, it is clear from (2) that a perturbation in the fine model space of corresponds to a perturbation in the coarse model space of .  This is logical since the matrix represents the most up-to-date approximation to the mapping between the two spaces.  Thus, the available information about the mapping between the two space is exploited.

The new extracted coarse model parameters either satisfy the success criterion or they are used to predict another candidate point which is then added to the set of points used for parameter extraction and the whole process is repeated.  See Fig. 1.  Using this recursive multi-point parameter extraction process improves the accuracy.  This may lead to the satisfaction of the success criterion or the step is declared a failure.  The step failure is declared in one of two cases: either the vector of extracted parameters approaches a limiting value with the success criterion not satisfied, or the number of fine model simulations since the last successful iteration has reached (n+1).  In the first case, the extracted coarse model parameters are trusted and the accuracy of the linearization used to predict  is suspected.  Thus to ensure a successful step from the current point , the trust region size is shrunk and a new suggested point is obtained.  In the latter case, sufficient information is available to obtain an estimate for the Jacobian of the fine model responses with respect to the fine model parameters.  This is done by solving the system of linear equations

’                                                       (3)

where is the kth candidate point used for multi-point parameter extraction and is the corresponding error between the fine model responses and the optimal coarse model responses.  This matrix is then used to make a step  in the parameter space by solving the system of equations

,                                                               (4)

varying parameter ( until  If there is no reduction in the l2 norm of the vector function g, the trust region is shrunk and (4) is resolved.  This is repeated until either the size of the trust region has shrunk significantly and hence the algorithm terminates or a successful step is taken.  This successful step is then used instead of the step obtained by (1) and the algorithm proceeds.

Double-folded Stub Filter

We consider the design of the double-folded stub (DFS) microstrip structure shown in Fig. 2 (Bandler et al. [5,6,7]).  Folding the stubs reduces the filter area w.r.t. the conventional double stub structure (Rautio [8]).  The filter is characterized by five parameters : W1 , W2 , S, L1 and L2  (see Fig. 2).  L1, L2 and S are chosen as optimization variables.  W1 and W2 are fixed at 4.8 mil.  The design specifications are given by (S21(( -3 dB in the passband and(S21(( -30 dB in the stopband, where the passband includes frequencies below 9.5 GHz and above 16.5 GHz and the stopband lies in the range [12 GHz, 14 GHz].  The structure is simulated by Sonnet’s em [9] through OSA’s Empipe [10].  The coarse model is a coarse-grid em model with cell size 4.8 mil by 4.8 mil.  The fine model is a fine-grid em model with cell size 1.6 mil by 1.6 mil.  Other parameters are summarized in Table I.

Table II shows the optimal coarse model parameters obtained by the OSA90/hope [10] minimax optimizer.  Fig. 3 shows the response along with the fine model em response evaluated using the optimal coarse model parameters.  The time needed to simulate the structure (coarse model) at a single frequency is only 5 CPU seconds on a Sun SPARCstation 10.  This includes the automatic response interpolation carried out to accommodate off-grid geometries.

It is clear from Fig. 3 that the fine model response violates the design specifications at the starting point.  The new ASM technique required only two iterations to reach the solution.  The algorithm’s progress is shown in Table III.  The number of required fine model simulations is 17.  Most of these simulations were needed for response interpolation.  The response of the fine model at the solution is shown in Fig. 4.  The CPU time needed for the fine model is approximately 70 seconds per frequency point.

Waveguide Transformer

We optimized a two-section waveguide transformer as shown in Fig. 5.  This example is a classical microwave circuit design problem [11] and is presented to illustrate the new ASM algorithm.  Here we use two empirical models: an ideal model which neglects the junction discontinuities and a nonideal model which includes the junction discontinuity effects [11].

The ideal (coarse) model is first optimized.  The results are shown in Table IV.  The optimum ideal model response is shown in Fig. 6 along with the nonideal model response at the same point.  Our algorithm terminated in three iterations, requiring 5 fine model simulations.  The optimal nonideal model design is given in Table V.   The corresponding nonideal model response is shown in Fig. 7.  This example is known to have more than one minimum for the parameter extraction step [2].  However, our new algorithm converged successfully to the optimal design.  The number of simulations needed to align the two models is smaller than that reported in [2].

HTS Filter

We consider optimization of a high-temperature superconducting (HTS) filter [1,12].  This filter is illustrated in Fig. 8.  The specifications are(S21(( 0.95 in the passband and (S21(( 0.05 in the stopband, where the stopband includes frequencies below 3.967 GHz and above 4.099 GHz and the passband lies in the range [4.008 GHz, 4.058 GHz].  The design variables for this problem are L1, L2, L3, S1, S2 and S3.  We take L0 = 50 mil and W = 7 mil.  The coarse model exploits the empirical models of microstrip lines, coupled lines and open stubs available in OSA90/hope.  The fine model employs a fine-grid em simulation.  The material and physical parameters values used in both OSA90/hope and in em are shown in Table VI.  The coarse model is first optimized using the OSA90/hope minimax optimizer.  The optimal coarse model design is given in Table VII.  The fine model response at the optimal coarse model design are shown in Fig. 9.  The parameter extraction for this problem has several solutions.  Fig. 10 shows how two of the extracted coarse model parameters changed with the number of points used for parameter extraction.  The first point (1) is obtained using normal parameter extraction.  These extracted values would have caused the original ASM technique to diverge.  The new technique automatically generates a candidate point which is then used together with the original point to carry out a multi-point parameter extraction and the second point (2) is obtained.  To confirm that this point is the required one a third candidate point is automatically generated and the extraction is repeated using the three points to obtain the third extracted point (3).  The second and third extracted points show that the extracted vector of coarse model parameters is approaching a limiting value and can thus be trusted.  The coarse model response corresponding to the three extracted points of Fig. 10 are shown in Fig. 11.

For the remaining iterations, single point parameter extraction worked well.  The fine model responses and the coarse model responses for the corresponding extracted points are shown in Fig. 12.  The optimal fine model design was obtained in 5 iterations which required 8 fine model simulations.  The optimal fine model design is given in Table VIII.  The fine model response at this design is shown in Fig. 13.  The passband ripples are shown in Fig. 14.

In the original space mapping approaches [1,12] this example required significant manual intervention to successfully complete the parameter extraction phase.  Furthermore, without such intervention the previous approaches would not work.

Conclusions

A powerful new algorithm implementing the aggressive space mapping technique is introduced.  It aims at automatically improving the uniqueness of the parameter extraction step, the most critical step in the space mapping process, and exploiting all available fine model simulations.  Through examples which have proved difficult in the past we show that the new ASM algorithm automatically overcomes the nonuniqueness of the parameter extraction step in a logical way.  We are currently testing the proposed algorithm using HP HFSS [13].

References

[1]	J.W. Bandler, R.M. Biernacki, S.H. Chen, R.H. Hemmers and K. Madsen, “Electromagnetic optimization exploiting aggressive space mapping,” IEEE Trans. Microwave Theory Tech., vol. 43, 1995, pp. 2874-2882.

[2]	J.W. Bandler, R.M. Biernacki and S.H. Chen, “Fully automated space mapping optimization of 3-D structures,” in IEEE MTT-S int. Microwave Symp. Dig. (San Francisco, CA), 1996, pp. 753-756.

[3]	J.J. Mor( and D.C. Sorenson, “Computing a trust region step,” SIAM J. Sci. Stat. Comp., vol. 4, 1983, pp. 553-572.

[4]	C.G. Broyden, “A class of methods for solving nonlinear simultaneous equations,” Math. Comp., vol. 19, 1965, pp. 577-593.

[5]	J.W. Bandler, R.M. Biernacki, S.H. Chen, P.A. Grobelny and R.H. Hemmers, “Space mapping technique for electromagnetic optimiztion,” IEEE Trans. Microwave Theory Tech., vol. 42, 1994, pp. 2536-2544.

[6]	J.W. Bandler, R.M. Biernacki, S.H. Chen, P.A. Grobelny and R.H. Hemmers, “Exploitation of coarse grid for electromagnetic optimization,” IEEE MTT-S Int. Microwave Symp. Dig (San Diego, CA), 1994, pp. 381-384.

[7]	J.W. Bandler, R.M. Biernacki, S.H. Chen, D.G. Swanson, Jr. 	and S. Ye, “Microstrip filter design using direct EM field simulation,” IEEE Trans. Microwave Theory Tech., vol. 42, 1994, pp. 1353-1359.

[8]	J.C. Rautio, Sonnet Software, Inc., 1020 Seventh North Street, Suite 210, Liverpool, NY 13088, Private Communication, 1992.

[9]	em , Sonnet Software, Inc., 1020 Seventh North Street, Suite 210, Liverpool, NY 13088, 1996.

[10]	OSA90/hope( and Empipe(, Optimization Systems Associates Inc., Ontario, Canada, 1997.

[11]	J.W. Bandler, “Computer optimization of inhomogeneous waveguide transformers,” IEEE Trans. Microwave Theory Tech., vol. MTT-17, 1969, pp. 563-571.

[12]	J.W. Bandler, R.M. Biernacki, S.H. Chen, W.J. Gestinger, P.A. Grobelny, C. Moskowitz and S.H. Talisa, “Electromagnetic design of high-temperature superconducting filters,” Int. J. Microwave and Millimeter-Wave Computer-Aided Engineering, vol. 5, 1995, pp. 331-343.

[13]	HFSS, Hewlett-Packard Co., 1400 Fountaingrove Parkway, Santa Rosa, CA 95403, 1997.

TABLE I

MATERIAL AND PHYSICAL PARAMETERS FOR THE COARSE

AND FINE em MODELS OF THE DFS FILTER

| Model Parameter | Value |
| --- | --- |
| substrate dielectric constant | 9.9 |
| substrate thickness (mil) | 5 |
| shielding cover height (mil) | ( |
| conducting material thickness | 3.0E-6 |
| substrate dielectric loss tangent | 2.0E-3 |
| resistivity of metal ((m) | 1.72E-8 |
| magnetic loss tangent | 0 |
| surface reactance ((/sq) | 0 |
| lower frequency limit (GHz) | 5 |
| upper frequency limit (GHz) | 20 |
| frequency increment size (GHz) | 0.25 |

TABLE II

OPTIMAL DESIGN OF THE COARSE MODEL

FOR THE DFS FILTER

| Parameter | Value (mil) |
| --- | --- |
| L1 | 88.8 |
| L2 | 84.1 |
| S | 3.9 |

TABLE III

VALUES OF DESIGNABLE PARAMETERS AT EACH ITERATION

FOR THE DFS FILTER

| Parameter |  |  |  |
| --- | --- | --- | --- |
| L1 | 88.8 | 89.5 | 94.3 |
| L2 | 84.1 | 84.6 | 85.4 |
| S | 3.9 | 4.7 | 4.7 |
| all values are in mils |

TABLE IV

OPTIMAL DESIGN OF THE COARSE (IDEAL) MODEL

FOR THE TWO-SECTION WAVEGUIDE TRANSFORMER

| Parameter | Value (cm) |
| --- | --- |
| a1 | 0.712 |
| b1 | 1.395 |
| a2 | 1.657 |
| b2 | 1.590 |

TABLE V

VALUES OF OPTIMIZABLE PARAMETERS

AT EACH ITERATION OF THE NEW ASM TECHNIQUE

FOR THE TWO-SECTION WAVEGUIDE TRANSFORMER

| Parameter |  |  |  |  |
| --- | --- | --- | --- | --- |
| a1 | 0.712 | 0.715 | 0.716 | 0.716 |
| b1 | 1.395 | 1.400 | 1.402 | 1.402 |
| a2 | 1.657 | 1.591 | 1.560 | 1.560 |
| b2 | 1.590 | 1.541 | 1.518 | 1.518 |
| all values are in cm |

TABLE VI

MATERIAL AND PHYSICAL PARAMETERS

FOR THE HTS FILTER

| Model Parameter | OSA90/hope | em |
| --- | --- | --- |
| substrate dielectric constant | 23.425 | 23.425 |
| substrate thickness (mil) | 19.9516 | 19.9516 |
| shielding cover height (mil) | ( | 250 |
| conducting material thickness | 1.968E-2 | 0 |
| substrate dielectric loss tangent | 3.0E-5 | 3.0E-5 |
| resistivity of metal ((m) | 0 | 4.032E-8 |
| surface roughness of metal | 0 | ( |
| magnetic loss tangent | ( | 0 |
| surface reactance ((/sq) | ( | 0 |
| x-grid cell size (mil) | ( | 1.00 |
| y-grid cell size (mil) | ( | 1.75 |

TABLE VII

THE OPTIMAL DESIGN OF THE COARSE MODEL

FOR THE HTS FILTER

| Parameter | Optimal Value (mil) |
| --- | --- |
| L1 | 188.33 |
| L2 | 197.98 |
| L3 | 188.58 |
| S1 | 21.97 |
| S2 | 99.12 |
| S3 | 111.67 |

TABLE VIII

THE INITIAL AND FINAL DESIGNS OF THE FINE MODEL

FOR THE HTS FILTER

| Parameter | Initial Value (mil) | Final Value (mil) |
| --- | --- | --- |
| L1 | 188.33 | 181.43 |
| L2 | 197.98 | 200.51 |
| L3 | 188.58 | 180.49 |
| S1 | 21.97 | 19.44 |
| S2 | 99.12 | 80.52 |
| S3 | 111.67 | 83.41 |

parameter extraction fails; an additional point        is obtained and multi-point parameter extraction is carried out to sharpen the solution

Fig. 1.  Illustration of the automated multi-point parameter extraction.

Fig. 2.  The DFS filter [8].

Fig. 3.  The optimal coarse model response (() and the fine model response (()

at the starting point for the DFS filter .

Fig. 4.  The optimal coarse model response (() and the optimal fine model

response (() for the DFS filter.

Fig. 6.  The optimal coarse model response (() and the fine model response (()

at the starting point for the two-section waveguide transformer.

Fig. 7.  The optimal coarse model response (() and the optimal fine model

response (() for the two-section waveguide transformer.

Fig. 8.  The structure of the HTS filter [12].

Fig. 9.  The optimal coarse model response (() and the fine model response (()

at the starting point for the HTS filter.

L1

Fig. 10.  The variation of two of the extracted coarse model parameters in the first iteration with the number of points used for parameter extraction where (1) is obtained using a  single fine model point, (2) is obtained using two fine model points and (3) is obtained using three fine model points.

(a)                                                                                  (b)

(c)

Fig. 11.  The coarse model response (() and the fine model response (() corresponding to the three extracted points in Fig. 10 where (a) is obtained using a single fine model, (b) is obtained using two fine model points and (c) is obtained using three fine model points.

(a)                                                                                  (b)

(c)                                                                                      (d)

Fig. 12. The coarse model response (() at the extracted point and the fine model

response (() corresponding to the second, third, fourth and fifth iterations.

Fig. 13.  The optimal coarse model response (() and the optimal fine model

response (() for the HTS filter.

Fig. 14. The optimal coarse model response (() and the optimal fine model

response (() for the HTS filter in the passband.

# Text boxes

xem,1

xem,2

xos,2

xem,2

xos,1

the current state at the ith iteration

xos,2

xem,1

xos,1

initial parameter extraction at the suggested point

xem,1

xem,2

xos,1

xos,2

S

W2

L1

L2

W1

Fig. 5.  A typical two-section waveguide transformer.

Lo

L1

L2

L3

L2

L1

Lo

S1

S2

S3

S2

S1

W

x

y

S3