A HYBRID AGGRESSIVE SPACE MAPPING

ALGORITHM FOR EM OPTIMIZATION

M.H. Bakr, J.W. Bandler, N. Georgieva and K. Madsen

SOS-99-9-R

March 1999

( M.H. Bakr, J.W. Bandler, N. Georgieva and K. Madsen 1998

No part of this document may be copied, translated, transcribed or entered in any form into any machine without written permission.  Address inquiries in this regard to Dr. J.W. Bandler.  Excerpts may be quoted for scholarly purposes with full acknowledgment of source.  This document may not be lent or circulated without this title page and its original cover.

A HYBRID AGGRESSIVE SPACE MAPPING(

ALGORITHM FOR EM OPTIMIZATION

Mohamed H. Bakr, Student Member, IEEE, John W. Bandler, Fellow, IEEE,

Natalia Georgieva, Member, IEEE, and Kaj Madsen

Abstract	We propose a novel Hybrid Aggressive Space Mapping (HASM) optimization algorithm.  HASM exploits both the Trust Region Aggressive Space Mapping (TRASM) strategy and direct optimization.  Severe differences between the coarse and fine models and nonuniqueness of the parameter extraction procedure may cause the TRASM algorithm to be trapped in local minima.  The HASM algorithm is based on a novel lemma that enables smooth switching from the TRASM optimization to direct optimization if the TRASM algorithm is not converging.  It also enables switching back from direct optimization to the TRASM algorithm in a smooth way.  The uniqueness of the extraction step is improved by utilizing a good starting point.  The algorithm does not assume that the final space-mapped design is the true optimal design and is robust against severe misalignment between the coarse and fine models.  The new algorithm has been tested on designs of several microwave filters and transformers.  The examples include a three-section and a seven-section waveguide transformer as well as the design of an H-plane waveguide filter and a double-folded stub filter.

I. INTRODUCTION

In this work a Hybrid Aggressive Space Mapping (HASM) algorithm is presented.  Space Mapping (SM) optimization [1-4] assumes that the circuit under consideration can be simulated using two models: a fine model and a coarse model.  The fine model is accurate but is computationally intensive, e.g., a full-wave EM simulator.  The coarse model is assumed to be fast but not very accurate.  SM optimization directs most of the optimization computational effort towards the coarse model while maintaining the accuracy of the fine model.  The overall computational effort needed is much smaller than that for direct optimization.

Parameter extraction is crucial to the Aggressive Space Mapping (ASM) technique [4].  Here, a coarse model point whose response matches a given fine model response is obtained.  This is essentially an optimization problem.  The nonuniqueness of the extracted parameters may lead to divergence or oscillation of the iterations [2].  To alleviate this problem the TRASM algorithm was introduced [3].  TRASM integrates a trust region methodology [5] with the ASM technique.  Also, it utilizes a recursive multi-point parameter extraction in order to improve the uniqueness of the extraction step.

In this work we address the convergence behavior of the TRASM algorithm.  We discuss the effect of a severely misaligned coarse model.  We show that in this case TRASM optimization may be trapped in local minima.

The design obtained by pure SM optimization in most cases is very near optimal.  However, the optimality of the final design can not be guaranteed.  This is because the final space-mapped response matches the optimal coarse model response, which may be different from the optimal fine model response obtained by solving the original design problem in the fine model space.

Our HASM algorithm is designed to overcome these limitations.  The algorithm switches smoothly between SM optimization and direct optimization and vice versa.  A novel lemma enables such a switch.  The algorithm also integrates a novel prediction of the starting point for the parameter extraction problem to enhance the uniqueness.

We start by giving a brief review of SM algorithms in Section II.  Some properties of SM optimization that justify utilizing a hybrid algorithm are discussed in Section III.  The novel lemma and the prediction approach are introduced in Sections IV and V, respectively.  The HASM algorithm is presented in Section VI.  The algorithm is applied successfully to the design of microwave transformers and filters.  The examples include the design of a three-section waveguide transformer, a seven-section waveguide transformer, an H-plane waveguide filter and a double-folded stub microstrip filter.  These examples are given in Section VII.  Finally, the conclusions are given in Section VIII.

II. SPACE MAPPING: A BRIEF REVIEW

We refer to the vectors of “fine” model parameters and “coarse” model parameters as and , respectively.  The first step in any SM algorithm is to obtain the optimal design of the coarse model .  The corresponding response is denoted by .  ASM aims at establishing a mapping P between the two spaces [4]

(1)

such that

(2)

where Rem is the vector of fine model response, Ros is the vector of coarse mode response and  is a suitable norm.  We define the error function

(3)

The final fine model design is obtained and the mapping is established by solving the nonlinear system

f(xem) = 0                                                                        (4)

Let  be the ith iterate in the solution of (4).  In the ASM technique, the next iterate  is found by a quasi-Newton iteration

(5)

where  is obtained from

(6)

and is an approximation to the Jacobian of the vector f with respect to  at the ith iteration.  The matrix B is updated at each iteration using Broyden’s update [6].

Vector f is obtained by evaluating , which is done indirectly through parameter extraction.  The nonuniqueness of this problem may lead to divergence or oscillation of the ASM technique.  The TRASM algorithm [3] was designed to overcome this problem.  At the ith iteration, the residual vector defines the difference between the vector of extracted coarse model parameters = and the optimal coarse model design.  The value  serves as a measure of the misalignment between the two spaces in the ith iteration.  The TRASM algorithm aims at minimizing .  The ith iteration of the algorithm is given by

(7)

Parameter ( is selected such that the step obtained satisfies  where (  is the size of the trust region.

III. SOME PROPERTIES OF SPACE MAPPING

ASM and TRASM are efficient algorithms.  The number of fine model simulations needed to obtain the space-mapped design is of the order of the problem dimensionality.  However, both algorithms depend on the existence of a coarse model that is fast and has enough accuracy.

# If the coarse model is bad (i.e., very different from the fine model) space mapping might not work.  To illustrate this we consider the Rosenbrock function [7].  We form an artificial problem in which the “coarse” model is given by

(8)

and the “fine” model by

(9)

where and  are constant shifts.  The target of the direct optimization problem is to minimize Rem.  Considering (8) and (9) we notice that  = [1.0   1.0]T and  = ((( ) where (  = [   ]T.  The misalignment between the two models is thus given by the two shifts and .

We discuss two sets of values for the shifts.  First, we consider ( = [(0.1   (0.1]T.  Using (8) and (9) we notice that the coarse model point whose response matches the fine response at a point  is = (+( ).  It follows that the mapping between the two spaces is given by .  The contours of  are shown in Fig. 1(a).  The mapping  is then approximated through multi-point parameter extraction [3].  Only one perturbed fine model point is utilized.  The contours of  obtained in this manner are shown in Fig. 1(b).  Figs. 1(a) and 1(b) show that  has a single minimum which is the solution that would have been obtained by direct optimization.  The differences between the two plots are attributed to the nonuniqueness of the parameter extraction process.  Taking the point  as the initial solution of the fine model, the TRASM algorithm is expected to converge to .  The corresponding contours of Rem are shown in Fig. 1(c), whose minimum value is at [1.1   1.1]T as expected.

The same steps are repeated for the case (  = [(1.5   (1.5]T.  The contour plot of  is shown in Fig. 2(a).  The contour plot of  obtained using parameter extraction is shown in Fig. 2(b).  Fig. 2(b) illustrates the existence of a minimum of  other than  which is closer to the starting point of the TRASM algorithm .  It follows that the TRASM algorithm is unlikely to converge to .  The corresponding contours of Rem for this case are shown in Fig. 2(c), whose minimum value is at [2.5   2.5]T.

The solution obtained using SM optimization is very near optimal if  is similar to the optimal fine model response .  However, this can not be guaranteed.  For example, consider

(10)

Assume also that

(11)

where ( > 0.  It is clear that  is equal to ( while  is zero.  It follows that space mapping may converge to a solution other than .

###### IV. SPACE MAPPING AND DIRECT OPTIMIZATION

The properties of space mapping suggest that a hybrid algorithm be used.  This algorithm exploits the efficiency of space mapping and defaults to direct optimization when space mapping fails.  Our HASM algorithm utilizes a novel lemma that enables smooth switching between the TRASM algorithm and direct optimization and vice versa.

Lemma Assume that  corresponds to  through a parameter extraction process.  Then the Jacobian of the fine model response at  and the Jacobian  of the coarse model response at  are related by

(12)

where B is a valid mapping between the two spaces at  and .

Proof

As the points  and correspond to each other, it follows that their responses match, i.e.,

(13)

Now define a new fine model point  where is a small perturbation.  The response at this new point is perturbed from the response at the point  by

(14)

The point corresponds to a coarse model point  that satisfies

(15)

Also, by definition of the mapping B the two perturbations andare related by

(16)

multiplying both sides of (16) by we get

(17)

Comparing (17) with (15) we conclude that

(18)

Relation (18) is interesting.  It shows that by having the matrix B and the coarse model Jacobian we are able to obtain a good estimate of the Jacobian of the fine model response without any further fine model simulations.  It follows that when SM optimization is not converging smoothly we can switch to direct optimization and supply it with the available first order derivatives given by (18).

Another relationship which can be easily obtained from (18) is

(19)

Relation (19) assumes that is  full rank and m ( n, where n is the number of parameters and m is the dimensionality of both  and .  It is used for switching back from direct optimization to SM optimization.  Fig. 3 illustrates the switching between SM optimization and direct optimization.

We illustrate the lemma as follows.  Consider

(20)

and

(21)

Take .  Here Rem = 4.82.  The solution for the parameter extraction problem is =[1.90    1.10]T.  The Jacobian at  is

(22)

From (20) and (21) it is seen that

(23)

It follows that at is estimated by

(24)

which is the exact Jacobian of the fine model response.

###### V. SELECTION OF THE STARTING POINT

The discussion in Section III reveals how the nonuniqueness of the parameter extraction process can affect the convergence of SM optimization.  The uniqueness of this procedure can be improved by utilizing a good starting point.  In the first iteration of the algorithm there is no available information about the mapping between the two spaces.  A reasonable assumption is to take  as the starting point for the parameter extraction optimization problem.  As the algorithm proceeds the matrix approximates the mapping between the two spaces.  A prediction of the extracted parameters in the ith iteration is given by

(25)

This predicted point is then taken as a starting point for the parameter extraction optimization problem.  It supplies a good starting point provided that  is a valid solution to the parameter extraction in the previous iteration and approximates the mapping between the two spaces.

###### VI. THE HASM ALGORITHM

The HASM algorithm exploits SM when effective, otherwise it defaults to direct optimization.  Two objective functions are utilized by the algorithm.  The first objective function is

(26)

while the second function is

(27)

While (26) aims at matching the extracted coarse model parameters to  in the parameter space, (27) aims at matching the same points mapped through the appropriate responses in the response space.

The HASM algorithm consists of two phases: the first phase follows the TRASM strategy while the second phase exploits direct optimization.  It utilizes (18) and (19) for switching between phases as dictated by the smoothness of convergence.

In the ith iteration we assume the existence of a trusted extracted coarse model parameters .  The step taken in this iteration is given by (7) where   Single-point parameter extraction is then applied at the point to get

The first phase utilizes two success criteria related to the reduction in (26) and (27).  The SM success criterion is defined as

(28)

which indicates that the actual reduction in the objective function (26) should be greater than a certain fraction of the predicted reduction.  The direct optimization success criterion is

(29)

which implies that the new iterate  is a descent iterate of (27).

The new point is accepted and the first phase resumes if this point satisfies both (28) and (29).  is then updated.  The vector  satisfying (28) is either obtained through single-point extraction or through recursive multi-point extraction [3] that approaches a limit satisfying (28).  We denote by and  the solution obtained at the end of the first phase and the corresponding fine model response, respectively.

Switching to the second phase takes place in two cases.  The first case is that (29) is not satisfied which means that we have to reject the new point .  The Jacobian of the fine model response at the point is then evaluated.  This is done by first evaluating the Jacobian of the coarse model response  at the previously extracted coarse model point =.   is then approximated using (18).  The second phase is then supplied by ,  and .

The second case occurs when the new point  satisfies (29) but does not satisfy (28).  In this case the point  is better than the previous point  and is accepted.  As the vector of extracted parameters does not satisfy (28), the vectorcan not be trusted.  In order to trust this vector, recursive multi-point parameter extraction is applied at the point  until eitherapproaches a limiting value or the number of additional points used for multi-point parameter extraction reaches n.  Ifapproaches a limit that does not satisfy (28),  is updated, at the extracted coarse model point = is evaluated and  is then approximated using (18).  Otherwise,  is approximated using the n+1 fine model points used for multi-point parameter extraction.  The second phase is then supplied by the point ,  and the Jacobian estimate, which is either calculated using (18) or through finite differences.

The second phase utilizes the first-order derivatives supplied by SM to carry out a number of successful iterations.  By a successful iteration we mean an iteration that satisfies the success criterion

(30)

which indicates that the actual reduction in the objective function (27) should be greater than a certain fraction of the predicted reduction.  Notice that the superscript k is used as an index for the successful iterates of the direct optimization phase.  At the end of each successful iteration parameter extraction is applied at the new iterate  and is used to check whether a switch back to the first phase can take place.  The criterion for such a switch is

(31)

If it is satisfied  is evaluated at the point =, B is reevaluated using (19) and the algorithm switches back to the first phase.  Otherwise, the second phase continues.  We denote by and the solution obtained at the end of the second phase and the corresponding fine model response, respectively.

For any iteration i ( 0, the two phases are given by the following steps.

Phase 1

Step 0	Given ,,and .  Set =.

Comment   is the utilized trust region size.

Step 1	Obtain by solving (7) with ( =.  Let .

Step 2	Evaluate using (5) and set .

Comment  V is the set of fine model points utilized in the multi-point extraction.

Step 3	Apply multi-point parameter extraction using the points in the set V to obtain .

Comment  The prediction given in (25) is used as a starting point for the multi-point parameter extraction.

Step 4	If both (28) and (29) are satisfied update the matrix tousing Broyden’s formula [6] and update (.  Go to Step 10.

Comment  The trust region size ( is updated based on how the predicted reduction in  agrees with the actual reduction [3].

Step 5	If (29) is not satisfied, obtain  and evaluate .  Switch to the second phase.

Comment  The second phase takes as arguments , and  and returns , and.  It should be clear that several iterations might be executed in the second phase before switching back to the first phase at Step 10.

Step 6	If  is equal to one, go to Step 9.

Comment   denotes the cardinality of the set V.

Step 7	Compare obtained using  fine model points with that previously obtained using (1 fine model points.  If  is approaching a limit, update the matrix to get , obtain , evaluate  and switch to the second phase.

Step 8	If  is equal to n+1, obtain the matrix  by finite differences using the set V.  Switch to the second phase.

Step 9	Obtain a temporary point  = , where

and .  Add this point to the set V and go to Step 3.

Step 10	Let i=i+1.  Go to Step 0.

The second phase can be summarized in the following steps.

Phase 2

Step 0	Given the current iterate of the space mapping technique , the corresponding Jacobian matrix  and

Step 1	Obtain a successful iterate  by solving

for a suitable value of  that satisfies the direct optimization success criterion.

Step 2	Update  to .

Step 3	Apply parameter extraction at  to get

Step 4	If (31) is satisfied obtain  at the point =, evaluate the matrix  and switch to the first phase.

Step 5	If the termination condition is satisfied invoke the minimax optimizer else set k=k+1 and go to Step 1.

A flow chart of the first phase of the HASM algorithm is shown in Fig. 4.

To ensure optimality, direct optimization is used to solve the original design problem using a minimax optimizer [8] starting from .  The current implementation of the HASM algorithm is in MATLAB [9].

###### VII. EXAMPLES

Three-Section Waveguide Transformer

We consider the design of a three-section waveguide transformer [10].  The design constraints are

VSWR ( 1.04  for 5.7 GHz ( f ( 7.2 GHz                                          (32)

The designable parameters are the heights of the waveguide sections b1, b2 and b3 and the lengths of waveguide sections L1, L2 and L3.  The fine model exploits HP HFSS [11] through HP Empipe3D [12].  The coarse analytical model does not take into account the junction discontinuity effects [10].

The vector  is taken as the initial fine model design (Fig. 5).  The HASM algorithm switched to the second phase after two iterations of the first phase, which required 4 fine model simulations.  The response  is shown in Fig. 6.  The second phase carried out only one iteration which required 2 fine model simulations.  The response is shown in Fig. 7.

Direct minimax optimization is then applied to the original design problem.  The optimal fine model response  is shown in Fig. 8.  Figs. 6 and 8 show that in this example  is different from .  The designs ,,and are shown in Table I.

###### Six-Section H-Plane Waveguide Filter

We consider a six-section H-plane waveguide filter [13, 14].  Design specifications are taken as

|S11| ( 0.16  for   5.4 GHz ( f ( 9.0 GHz                                          (33)

|S11| ( 0.85  for f ( 5.2 GHz  and |S11| ( 0.5  for 9.5 GHz ( f                             (34)

A waveguide with a cross-section of 1.372 inches by 0.622 inches (3.485 cm by 1.58 cm) is used.  The six sections are separated by seven H-plane septa, which have a finite thickness of 0.02 inches (0.508 mm).  The filter is shown in Fig. 9.

The optimizable parameters are the four septa widths W1, W2, W3 and W4 and the three waveguide-section lengths L1, L2 and L3.  The coarse model consists of lumped inductances and dispersive transmission line sections.  It is simulated using OSA90/hope [15].  There are various approaches to calculate the equivalent inductive susceptance corresponding to an H-plane septum.  We utilize a simplified version of a formula due to Marcuvitz [16] in evaluating the inductances.  The coarse model is shown in Fig. 10.  The fine model exploits HP HFSS [11] through HP Empipe3D [12].

The fine model response at the starting point  is shown in Fig. 11.  The first phase required 4 iterations to reach the design .  A total of 5 fine model simulations were needed.  The second phase did not carry out any successful iteration.  The response is shown in Fig. 12.

The response is obtained through direct minimax optimization (see Fig. 13).  The different fine model designs are given in Table II.  It is clear that the convergence of the first phase is smooth as ((.

Seven-Section Waveguide Transformer

The design of a seven-section waveguide transformer is also considered.  The transformer is shown in Fig. 14.  This example is a classical microwave circuit design problem [10].  The fine model is simulated using HP HFSS [11] through HP Empipe3D [12].  The coarse model is an analytical model which neglects the junction discontinuity [10].  The design specifications are taken as

VSWR ( 1.01  for  1.06 GHz ( f ( 1.8 GHz                                               (35)

The designable parameters for this problem are the height and length of each waveguide section.  The fine model response at  is shown in Fig. 15.  The first phase executed three successful iterations that required six fine model simulations.  The response  is shown in Fig. 16.  The second phase executed four iterations (see Fig. 17).  The response  is shown in Fig. 18.  Table III shows the different designs.

Double-Folded Stub Filter

We consider the design of the double-folded stub (DFS) microstrip structure (Bandler et al. [1]).  Folding the stubs reduces the filter area w.r.t. the conventional double stub structure (Rautio [17]).  The filter is characterized by five parameters : W1, W2, S, L1 and L2 (see Fig. 19).  L1, L2 and S are chosen as optimization variables.  W1 and W2 are fixed at 4.8 mil.  The design specifications are

(S21(( (3 dB  for  f ( 9.5 GHz  and 16.5 GHz ( f                                     (36)

(S21(( (30 dB  for  12 GHz ( f ( 14 GHz                                          (37)

The fine model is the structure simulated by HP HFSS [11] through HP Empipe3D [12].  The coarse model exploits the microstrip line and microstrip T-junction models available in OSA90/hope [15].  The coupling between the folded stubs and the microstrip line is simulated using equivalent capacitors.  The values of these capacitors are determined using Walker’s formulas [18].  Jansen’s microstrip bend model [19] is used to model the folding effect of the stub.  The coarse model is shown in Fig. 20.

The fine model response at  is shown in Fig. 21.  This figure shows a big shift between the optimal coarse response and the initial fine response.  This signals considerable misalignment between the two models.

The first phase successfully carried out eight iterations that required twelve fine model simulations.  The response  is shown in Fig. 22.  Fig. 23 shows a coarse contour plot of  in the neighborhood of the point of .  It is clear from this figure that the first phase was trapped in a local minimum.  The mapping established in the first phase is utilized to get a good estimate of  and a switch to the second phase is carried out.  The response  (Fig. 24) shows a significant improvement in the response.  The design  is then taken as the starting point for the minimax optimizer.  The response  is shown in Fig. 25.  The designs are given in Table IV.

###### VIII. CONCLUSIONS

We present a novel Hybrid Aggressive Space Mapping (HASM) optimization algorithm.  The algorithm is designed to handle severely misaligned cases.  It enables smooth switching from SM optimization to direct optimization if SM fails.  The direct optimization phase utilizes all the available information accumulated by SM optimization about the mapping between the coarse and fine model spaces.  The algorithm also enables switching back from direct optimization to space mapping if SM is converging smoothly.  The connection between SM and direct optimization is based on a novel lemma.  An original approach for the prediction of the starting point of the parameter extraction optimization problem is also utilized.  This approach improves the uniqueness of the extraction step and consequently enhances the convergence of the algorithm.  The algorithm is successfully demonstrated through the design of waveguide transformers and filters.

ACKNOWLEDGEMENT

The authors thank HP EEsof, Santa Rosa, CA, for making HP HFSS and HP Empipe3D available for this work.

###### REFERENCES

[1]	J.W. Bandler, R.M. Biernacki, S.H. Chen, P.A. Grobelny and R.H. Hemmers, “Space mapping technique for electromagnetic optimization,” IEEE Trans. Microwave Theory Tech., vol. 42, 1994, pp. 2536-2544.

[2]	J.W. Bandler, R.M. Biernacki and S.H. Chen, “Fully automated space mapping optimization of 3D structures,” IEEE MTT-S Int. Microwave Symp. Dig. (San Francisco, CA), 1996, pp. 753-756.

[3]	M.H. Bakr, J.W. Bandler, R.M. Biernacki, S.H. Chen and K. Madsen, “A trust region aggressive space mapping algorithm for EM optimization,” IEEE Trans. Microwave Theory Tech., vol. 46, 1998, pp. 2412-2425.

[4]	J.W. Bandler, R.M. Biernacki, S.H. Chen, R.H. Hemmers and K. Madsen, “Electromagnetic optimization exploiting aggressive space mapping,” IEEE Trans. Microwave Theory Tech., vol. 43, 1995, pp. 2874-2882.

[5]	J.J. Moré and D.C. Sorenson, “Computing a trust region step,” SIAM J. Sci. Stat. Comp., vol. 4, 1983, pp. 553-572.

[6]	C.G. Broyden, “A class of methods for solving nonlinear simultaneous equations,” Math. Comp., vol. 19, 1965, pp. 577-593.

[7]	R. Fletcher, Practical Methods of Optimization, New York: Wiley, Second Edition, 1987.

[8]	J.W. Bandler, W. Kellermann and K. Madsen, “A superlinearly convergent minimax algorithm for microwave circuit design,” IEEE Trans. Microwave Theory Tech., vol. MTT-33, 1985, pp. 1519-1530.

[9]	MATLAB( Version 5.0, The Math. Works, Inc., 24 Prime Park Way, Natick, MA 01760, 1997.

[10]	J.W. Bandler, “Computer optimization of inhomogeneous waveguide transformers,” IEEE Trans. Microwave Theory Tech., vol. MTT-17, 1969, pp. 563-571.

[11]	HP HFSS( Version 5.2, HP EEsof Division, 1400 Fountaingrove Parkway, Santa Rosa, CA 95403-1799, 1998.

[12]	HP Empipe3D( Version 5.2, HP EEsof Division, 1400 Fountaingrove Parkway, Santa Rosa, CA 95403-1799, 1998.

[13]	L. Young and B.M. Schiffman, “A useful high-pass filter design,” Microwave J., vol. 6, 1963, pp. 78-80.

[14]	G.L. Matthaei, L. Young and E.M. T. Jones, Microwave Filters, Impedance-Matching Network and Coupling Structures.  New York: McGraw-Hill, First Edition, 1964.

[15]	OSA90/hope( Version 4.0, formerly Optimization Systems Associates Inc., P.O. Box 8083, Dundas, ON, Canada, L9H 5E7, 1997, now HP EEsof Division, 1400 Fountaingrove Parkway, Santa Rosa, CA 95403-1799.

[16]	N. Marcuvitz, Waveguide Handbook.  New York: McGraw-Hill, First Edition, 1951, p. 221.

[17]	J.C. Rautio, Sonnet Software, Inc., 1020 Seventh North Street, Suite 210, Liverpool, NY 13088, Private Communication, 1992.

[18]	C.S. Walker, Capacitance, Inductance and Crosstalk Analysis, Norwood, MA: Artech House, 1990.

[19]	M. Kirschning, R. Jansen and N. Koster, “Measurement and computer-aided modeling of microstrip discontinuities by an improved resonator method,” IEEE MTT-S Int. Microwave Symp. Dig. (Boston, MA), 1983, pp. 495-497.

TABLE I

THE OPTIMAL COARSE MODEL DESIGN AND THE DESIGNS

OBTAINED DURING DIFFERENT PHASES OF THE HASM ALGORITHM FOR

THE THREE-SECTION WAVEGUIDE TRANSFORMER

| Parameter |  |  |  |  |
| --- | --- | --- | --- | --- |
| b1 | 0.90318 | 0.90331 | 0.90114 | 0.90549 |
| b2 | 1.37093 | 1.36436 | 1.35687 | 1.35777 |
| b3 | 1.73609 | 1.73208 | 1.72470 | 1.71866 |
| L1 | 1.54879 | 1.46991 | 1.47203 | 1.47008 |
| L2 | 1.58375 | 1.56402 | 1.56521 | 1.57587 |
| L3 | 1.64590 | 1.79666 | 1.77744 | 1.78286 |
| All values are in cm |

TABLE II

THE OPTIMAL COARSE MODEL DESIGN, THE FINAL SPACE-MAPPED

AND THE OPTIMAL FINE MODEL DESIGNS FOR THE

SIX-SECTION H-PLANE WAVEGUIDE FILTER

| Parameter |  | , |  |
| --- | --- | --- | --- |
| W1 | 0.48583 | 0.51326 | 0.51344 |
| W2 | 0.43494 | 0.47379 | 0.47396 |
| W3 | 0.40433 | 0.45091 | 0.45100 |
| W4 | 0.39796 | 0.44675 | 0.44664 |
| L1 | 0.65585 | 0.63701 | 0.63695 |
| L2 | 0.65923 | 0.63954 | 0.63977 |
| L3 | 0.67666 | 0.65704 | 0.65694 |
| All values are in inches |

TABLE III

THE OPTIMAL COARSE MODEL DESIGN AND THE DESIGNS

OBTAINED DURING DIFFERENT PHASES OF THE HASM ALGORITHM FOR

THE SEVEN-SECTION WAVEGUIDE TRANSFORMER

| Parameter |  |  |  |  |
| --- | --- | --- | --- | --- |
| b1 | 7.86732 | 7.84126 | 7.84321 | 7.84319 |
| b2 | 6.61888 | 6.56661 | 6.56753 | 6.56746 |
| b3 | 4.68540 | 4.63369 | 4.63275 | 4.63267 |
| b4 | 2.91987 | 2.88266 | 2.88266 | 2.88268 |
| b5 | 1.81412 | 1.79307 | 1.79273 | 1.79272 |
| b6 | 1.27658 | 1.26697 | 1.26721 | 1.26723 |
| b7 | 1.06847 | 1.06475 | 1.06477 | 1.06474 |
| L1 | 7.10588 | 7.27059 | 7.27141 | 7.27145 |
| L2 | 7.12201 | 7.03866 | 7.04043 | 7.04047 |
| L3 | 7.11760 | 6.89568 | 6.89549 | 6.89552 |
| L4 | 7.12331 | 6.89253 | 6.89192 | 6.89189 |
| L5 | 7.12815 | 6.98273 | 6.97985 | 6.98000 |
| L6 | 7.12154 | 7.03160 | 7.03020 | 7.03023 |
| L7 | 7.12945 | 7.02606 | 7.02503 | 7.02509 |
| All values are in cm |

TABLE IV

THE OPTIMAL COARSE MODEL DESIGN, THE FINAL SPACE-MAPPED

AND THE OPTIMAL FINE MODEL DESIGNS FOR THE

DFS FILTER

| Parameter |  |  |  |  |
| --- | --- | --- | --- | --- |
| L1 | 66.727 | 72.454 | 73.869 | 78.964 |
| L2 | 60.228 | 72.728 | 82.939 | 81.210 |
| S | 9.592 | 7.621 | 8.170 | 7.901 |
| All values are in mil |

Fig. 4.  A flow chart of the first phase of the proposed algorithm.

Fig. 9.  The fine model of the six-section H-plane waveguide filter [13, 14].

Fig. 10.  The coarse model of the six-section H-plane waveguide filter [16].

Fig. 11.  The coarse response  (() and the fine response  (() for the six-section H-plane waveguide filter.

Fig. 12.	The coarse response  (() and the fine response  (() for the six-section H-plane waveguide filter.

Fig. 13.	The coarse response  (() and the fine response  (() for the six-section H-plane waveguide filter.

Fig. 14.  The seven-section waveguide transformer [10].

Fig. 15.	The coarse response  (() and the fine response  (() for the seven-section waveguide transformer.

Fig. 16.	The coarse response  (() and the fine response  (() for the seven-section waveguide transformer.

Fig. 17.	The coarse response  (() and the fine response  (() for the seven-section waveguide transformer.

Fig. 18.	The coarse response  (() and the fine response  (() for the seven-section waveguide transformer.

Fig. 19.  The DFS filter [1, 17].

Fig. 20.  The coarse model of the DFS filter.

Fig. 21.  The coarse response  (() and the fine response  (() for the DFS filter.

Fig. 22.  The coarse response  (() and the fine response  (() for the DFS filter.

Fig. 23.	A coarse contour plot of  in the neighborhood of  for the DFS filter.

Fig. 24.	The coarse response  (() and the fine response  (() for the DFS filter.

Fig. 25.	The coarse response  (() and the fine response  (() for the DFS filter.

# Footnotes

This work was supported in part by the Natural Sciences and Engineering Research Council of Canada under Grants OGP0007239, STP0201832 and through the Micronet Network of Centres of Excellence.  N. Georgieva is supported by an NSERC Postdoctorate Fellowship and M.H. Bakr by an Ontario Graduate Scholarship.

M.H. Bakr, J.W. Bandler and N. Georgieva are with the Simulation Optimization Systems Research Laboratory and the Department of Electrical and Computer Engineering, McMaster University, Hamilton, Ontario, Canada, L8S 4K1.

J.W. Bandler is also with Bandler Corporation, P.O. Box 8083, Dundas, Ontario, Canada L9H 5E7.

K. Madsen is with the Department of Mathematical Modelling, Technical University of Denmark, DK-2800 Lyngby, Denmark.

# Text boxes

6.5

72.45

Fig. 6.	The coarse response  (() and the fine response  (() for the three-section waveguide transformer.

frequency (GHz)

7.3

Yes

VSWR

-80

VSWR

L2

L1

72.3

72.9

72.8

72.7

72.6

72.5

72.4

72.80

7.1

72.75

72.70

72.65

72.60

3.0

(a)

(a)

x2

3.0

2.5

2.0

1.5

1.0

0.5

0

6.9

3.0

2.5

2.0

1.5

1.0

0.5

0

-0.5

-1.0

x1

2.5

1.5

0

2.0

1.0

6.7

0.5

3.0

2.5

2.0

1.5

1.0

0.5

0

-80

VSWR

-80

VSWR

1.05

x2

3.0

72.40

2.5

2.0

1.5

1.0

0.5

0

3.0

2.5

2.0

1.5

1.0

0.5

0

-0.5

-1.0

Fig. 5.  The coarse response  (() and the fine response  (() for the three-section waveguide transformer.

x1

Fig. 2.  Different contour plots for the Rosenbrock problem for the case ( = [(1.5   (1.5]T; (a) the contour plot of , (b) the contour plot of  obtained through parameter extraction and (c) contours of the fine model Rosenbrock function.

(b)                                                                                            (c)

(S21(dB

0

-10

-20

-30

-40

-50

-60

-70

frequency (GHz)

5

20

17

14

11

8

(S21(dB

0

-10

-20

-30

-40

-50

-60

-70

frequency (GHz)

5

20

17

14

11

8

(S21(dB

0

-10

-20

-30

-40

-50

-60

-70

frequency (GHz)

5

20

17

14

11

8

(S21(dB

0

-10

-20

-30

-40

-50

-60

-70

frequency (GHz)

5

20

17

14

11

8

W1

L2

L1

W2

S

1.05

1.04

1.03

1.02

1.01

1.00

frequency (GHz)

1.9

1.8

1.7

1.6

1.5

1.4

1.3

1.2

1.1

1.0

1.05

1.04

1.03

1.02

1.01

1.00

frequency (GHz)

1.9

1.8

1.7

1.6

1.5

1.4

1.3

1.2

1.1

1.0

1.05

1.04

1.03

1.02

1.01

1.00

frequency (GHz)

1.9

1.8

1.7

1.6

1.5

1.4

1.3

1.2

1.1

1.0

1.04

1.03

1.02

1.01

1.00

frequency (GHz)

1.9

1.8

1.7

1.6

1.5

frequency (GHz)

7.3

7.1

6.9

6.7

6.5

Yes

Given,,and Set=

Evaluate using space mapping and set

Obtainusing the points in V

Both success

criteria satisfied?

No

Direct optimization success criterion is satisfied ?

Evaluate fromand

6.3

6.1

5.9

5.7

5.5

5.3

# VSWR

1.00

1.05

1.10

1.15

1.20

No

Yes

(V(=1?

No

Parameter extraction

is approaching a limit ?

Yes

Update B to get and obtain  using and

(V(=n+1?

No

Obtain a temporary point and set

Obtain  using the points in V

Yes

No

##### Phase 2

Update and

Set i=i+1

x2

x1

Direct Optimization

x, Jem

Space Mapping

x, f, B

-1.0

-0.5

x1

Fig. 3.  Illustration of the connection between SM optimization and direct optimization.

72.50

72.55

x1

x1

1.4

1.3

1.2

1.1

1.0

-80

(S11(

1.0

0.8

0.6

0.4

0.2

0

frequency (GHz)

9.50

8.64

7.78

6.92

6.06

5.20

(S11(

frequency (GHz)

1.0

0.8

0.6

0.4

0.2

0

9.50

8.64

7.78

6.92

6.06

5.20

(S11(

1.0

0.8

0.6

0.4

0.2

0

frequency (GHz)

9.50

8.64

7.78

6.92

6.06

5.20

(b)                                                                                          (c)

Fig. 8.  The coarse response  (() and the fine response  (() for the three-section waveguide transformer.

frequency (GHz)

7.3

7.1

6.9

6.7

6.5

6.3

6.1

5.9

5.7

5.5

5.3

# VSWR

1.00

1.05

1.10

1.15

1.20

Fig. 1.	Different contour plots for the Rosenbrock problem for the case ( = [(0.1   (0.1]T; (a) the contour plot of , (b) the contour plot of  obtained through parameter extraction and (c) contours of the fine model Rosenbrock function.

Fig. 7.  The coarse response  (() and the fine response  (() for the three-section waveguide transformer.

frequency (GHz)

7.3

7.1

6.9

6.7

6.5

6.3

6.1

5.9

5.7

5.5

5.3

# VSWR

1.00

1.05

1.10

1.15

1.20

1.20

6.3

6.1

5.9

5.7

5.5

5.3

# VSWR

1.00

1.05

1.10

1.15