AN AGGRESSIVE APPROACH TO

PARAMETER EXTRACTION

M.H. Bakr, J.W. Bandler and N. Georgieva

SOS-99-20-V

June 1999

( M.H. Bakr, J.W. Bandler and N. Georgieva 1999

No part of this document may be copied, translated, transcribed or entered in any form into any machine without written permission.  Address enquiries in this regard to Dr. J.W. Bandler.  Excerpts may be quoted for scholarly purposes with full acknowledgement of source.  This document may not be lent or circulated without this title page and its original cover.

AN AGGRESSIVE APPROACH TO

###### PARAMETER EXTRACTION

##### M.H. Bakr, J.W. Bandler and N. Georgieva

Simulation Optimization Systems Research Laboratory

and Department of Electrical and Computer Engineering

McMaster University, Hamilton, Canada L8S 4K1

bandler@mcmaster.ca

www.sos.mcmaster.ca

presented at

1999 IEEE MTT-S International Microwave Symposium, Anaheim, CA, June 14, 1999

The Parameter Extraction Problem

given a vector of measurements Rm , it is required to find a set of parameters of a model whose response matches Rm

it can be formulated as

where Ros is the vector of circuit response and  is the vector of extracted parameters

in the context of Space Mapping (SM) the fine model response Rem, typically from an electromagnetic simulator, at a certain point  supplies the target response Rm

multi-point parameter extraction enhances the uniqueness of the extraction problem and can be formulated as

where

and

, i=1, 2, . . ., Np

Illustration of Parameter Extraction

Classification of the Solution of Parameter Extraction

using a vector of matched responses R, a solution  of the parameter extraction problem is obtained

this solution is labeled locally unique if there exists an open neighborhood of  containing no other point  such that

the local uniqueness condition is equivalent to the condition that the Jacobian of the vector of matched coarse model responses R has rank n, where n is the number of optimizable parameters

locally nonunique                           locally unique

Problem Definition

## assume that multi-point parameter extraction is carried out at  using Np fine model points

then the vector of matched coarse model responses R is given by

where ; the set of perturbations utilized

it is required to find the perturbation  that can be added to the set and significantly enhances the uniqueness of the extraction step

Problem Assumptions

the coarse model is assumed to be much faster than the fine model

few extra coarse model simulations add negligible overhead to the computational time of the problem

the first and second order derivatives of the coarse model responses can be obtained

in the absence of information about the mapping between the two spaces we take B=I

the mapping B can be integrated with the algorithm if it is available

The Locally Nonunique Case

assume that the rank of the Jacobian of matched coarse model responses at  is k < n

we impose the condition that the gradients of n(k of the responses generated by the new coarse model point + be normal to the gradients of a linearly independent set of gradients of cardinality k of the responses in the vector R

define the set of linearly independent gradients by

the gradient of each of the n(k selected responses can be approximated by

,  i=k+1, . . ., n

where is the gradient of the ith response at  and is the corresponding Hessian

The Locally Nonunique Case

the perturbation  that satisfies the orthogonality condition is obtained by solving

where

A=[]

and

this system of linear equations may be under-determined, over-determined or well-determined

the pseudoinverse of AT is used to find the solution of minimum length in all cases

is rescaled to satisfy a certain trust region condition

The Locally Unique Case

a perturbation of  results in a perturbation of the coarse model response at the two minima by

and

we impose the condition that the difference between the  norms of these two response perturbations be maximized subject to certain trust region size

it follows that the following Lagrangian can be formed

it can be shown that the perturbation  is an eigenvector for the matrix

the perturbation is then scaled to satisfy the length condition

we make the assumption that  because of lack of information about other minima

The Algorithm Flowchart

An Illustration of the Algorithm

A Quadratic Function

the coarse model is

the fine model is taken as

it is required to extract the coarse model parameters corresponding to xem=[2.0    1.0]T

4 fine model points were needed to ensure the uniqueness of the extracted parameters

The Variation of the Extracted Parameters with the Number of Fine Model Points for the Quadratic Function

| Number of Points |  |  |
| --- | --- | --- |
| 1 | 1.95724 | 0.99458 |
| 2 | 2.10283 | 0.63094 |
| 3 | 1.92787 | 1.05337 |
| 4 | 1.89571 | 1.10868 |

the exact solution for the parameter extraction problem is

T

Contours of the  Objective Function for the Quadratic Function

single-point extraction

Contours of the  Objective Function for the Quadratic Function

three-point extraction

four-point extraction

The Rosenbrock Function

the coarse model is

the fine model is

it is required to extract the vector of coarse model parameters at the point

3 fine model points were needed for the algorithm to terminate

the variation of the extracted parameters with the number of fine model points is shown in the table

| Number of Points |  |  |
| --- | --- | --- |
| 1 | 1.21541 | 0.91728 |
| 2 | 0.80008 | 1.20012 |
| 3 | 0.80008 | 1.20014 |

Contours of the  Objective Function for the Rosenbrock Function

single-point extraction

Contours of the  Objective Function for the Rosenbrock Function

three-point extraction

10:1 Impedance Transformer

the design parameters are the characteristic impedances of the two transmission lines

the lengths of both lines are kept fixed at their optimal values (quarter wavelength)

the coarse model is an ideal 10:1 impedance transformer

the fine model scales each of the two impedances by 1.6

the responses of both models at 11 different frequencies in the frequency band  0.5 GHz ( f ( 1.5 GHz were used to match the two models

it is required to extract the coarse model parameters corresponding to the fine model point [2.2628   4.5259]T

3 fine model points were needed to improve uniqueness

The Matched Responses for the 10:1 Transformer (Single-Point Extraction)

the set of fine model points utilized in parameter extraction is

the extracted parameters are

Contours of the  Objective Function for the 10:1 Transformer (Single-Point Extraction)

The Matched Responses for the 10:1 Transformer (Two-Point Extraction)

the set of fine model points utilized in parameter extraction is

the extracted parameters are

Contours of the  Objective Function for the 10:1 Transformer (Two-Point Extraction)

The Matched Responses for the 10:1 Transformer (Three-Point Extraction)

the set of fine model points is

the extracted parameters are

Contours of the  Objective Function for the 10:1 Transformer (Three-Point Extraction)

HTS Filter

(Westinghouse, 1993, Bandler et al., 1995)

the fine model simulates the filter as a whole

the coarse model is a decomposed version of the fine model with coarser grid size

both models exploit Sonnet’s em

it is required to extract the coarse model point corresponding to

xf =  =

HTS Filter

4 fine model points are needed to trust the extracted parameters

| Parameter |  |  |  |  |
| --- | --- | --- | --- | --- |
| L1 | 181.00 | 182.55 | 181.34 | 179.86 |
| L2 | 201.59 | 205.64 | 205.38 | 197.74 |
| L3 | 180.97 | 183.36 | 184.20 | 178.08 |
| S1 | 20.12 | 20.05 | 20.07 | 20.46 |
| S2 | 67.89 | 68.40 | 68.08 | 67.35 |
| S3 | 66.85 | 67.25 | 66.98 | 66.46 |
| all values are in mils |

| Parameter | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| L1 | 188.31 | 179.99 | 176.67 | 178.50 |
| L2 | 197.69 | 204.52 | 208.52 | 206.78 |
| L3 | 189.72 | 181.230 | 178.00 | 179.09 |
| S1 | 19.34 | 17.13 | 17.21 | 18.99 |
| S2 | 52.67 | 63.44 | 56.52 | 57.99 |
| S3 | 52.06 | 53.18 | 53.47 | 56.77 |
| all values are in mils |

The Matched Responses for the HTS Filter

single point extraction

two-point extraction

The Matched Responses for the HTS Filter

three-point extraction

The Matched Responses for the HTS Filter

four-point extraction

Double-Folded Stub Microstrip Filter

(Bandler et al., 1994)

the fine model is the structure simulated by HP HFSS through HP Empipe3D

the coarse model exploits the microstrip line and microstrip T-junction models available in OSA90/hope

the coupling between the folded stubs and the microstrip line is simulated using equivalent capacitors (Walker, 1990)

Double-Folded Stub Microstrip Filter

the folding effect of the stub is included utilizing the bend model (Jansen et al., 1983)

W1 and W2 are fixed at 4.8 mil

it is required to extract the coarse model parameters corresponding to the fine model point

[L1  L2  S]T = [66.73  60.23  9.59]T mils

Double-Folded Stub Microstrip Filter

9 fine model points are needed to ensure the uniqueness of the extracted parameters

| Parameter |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L1 | 66.73 | 67.72 | 67.32 | 66.15 | 70.60 | 67.66 | 62.82 | 65.80 | 66.57 |
| L2 | 60.23 | 63.58 | 64.13 | 56.33 | 59.48 | 64.10 | 60.88 | 56.36 | 59.85 |
| S | 9.59 | 9.27 | 9.48 | 9.71 | 9.71 | 9.66 | 9.50 | 9.52 | 10.26 |
| all values are in mils |

| Parameter |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L1 | 58.01 | 67.05 | 66.11 | 64.36 | 56.46 | 66.10 | 56.50 | 56.39 | 56.59 |
| L2 | 38.40 | 40.47 | 40.40 | 43.28 | 42.94 | 42.02 | 42.81 | 43.00 | 43.02 |
| S | 3.24 | 6.86 | 6.64 | 8.83 | 18.10 | 7.99 | 18.25 | 17.93 | 17.87 |
| all values are in mils |

Matched Responses of the Coarse and Fine Models

the given fine model response and the coarse

model response at

The Variation of the Objective Function with the Number of Fine Model Points

at the point  (( ( () and at the point  (( ( ()

Conclusions

we present an Aggressive Parameter Extraction (APE) algorithm

the APE algorithm addresses optimal selection of parameter perturbations to improve the sharpness of a multi-point parameter extraction procedure

new parameter perturbations are generated based on the nature of the minimum reached in the previous iteration

we consider possibly locally unique and locally nonunique minima

the APE algorithm continues until the extracted coarse model parameters can be trusted

the algorithm is demonstrated through a number of examples

# Text boxes

1.6

Apply multi-point parameter extraction using the points in the set  to get

Yes

No

Yes

Stop

Obtain a new perturbation using second method. Set  and i=i+1

Is  approaching a limit ?

No

Yes

Is =1?

Obtain a new perturbation using first method.  Set   and i=i+1

No

J() has rank n ?

Given , (  and n.

Initialize i=1 and

Fifth Section

Fourth Section

Third

Section

Second Section

First Section

y

x

W

S1

S2

S3

S2

S1

L0

L1

L2

L3

L2

L1

L0

(S21( dB

0

-10

-20

-30

-40

-50

-60

frequency (GHz)

4.179

4.117

4.054

3.992

3.929

3.867

(S21( dB

0

-10

-20

-30

-40

-50

-60

frequency (GHz)

4.179

4.117

4.054

3.992

3.929

3.867

(S21( dB

0

-10

-20

-30

-40

-50

-60

frequency (GHz)

4.179

4.117

4.054

3.992

3.929

3.867

(S21( dB

0

-10

-20

-30

-40

-50

-60

frequency (GHz)

4.179

4.117

4.054

3.992

3.929

3.867

(S21( dB

0

-10

-20

-30

-40

-50

-60

frequency (GHz)

4.179

4.117

4.054

3.992

3.929

3.867

(S21( dB

0

-10

-20

-30

-40

-50

-60

frequency (GHz)

4.179

4.117

4.054

3.992

3.929

3.867

(S21( dB

0

-10

-20

-30

-40

-50

-60

frequency (GHz)

4.179

4.117

4.054

3.992

3.929

3.867

(S21( dB

0

-10

-20

-30

-40

-50

-60

frequency (GHz)

4.179

4.117

4.054

3.992

3.929

3.867

(S21( dB

0

-10

-20

-30

-40

-50

-60

frequency (GHz)

4.179

4.117

4.054

3.992

3.929

3.867

(S21( dB

0

-10

-20

-30

-40

-50

-60

frequency (GHz)

4.179

4.117

4.054

3.992

3.929

3.867

single-point extraction

#### B

xem

Rem

0

### V

1.6

xem,2

xem,1

xos

Ros

xos,2

xos,1

e

0.8

2.0

0.4

2.0

1.2

e

xos

u1

xos,2

xos,1

xem

u2

xem,2

xem,1

multi-point extraction

1.2

0.8

0.4

0

x2

x1

4

2

0

-2

-4

4

2

0

-2

-4

x2

x1

4

2

0

-2

-4

4

2

0

-2

-4

x2

x1

4

2

0

-2

-4

4

2

0

-2

-4

two-point extraction

x2

x1

4

2

0

-2

-4

4

2

0

-2

-4

x2

x1

4

2

0

-2

-4

4

2

0

-2

-4

u2

u2

u2

(S11(

(S11(

(S11(

Z2

0.4

(S11(

Z2

(S11(

Z2

Z1

10

9

8

7

6

5

4

3

2

1

7

6

5

4

3

2

1

Z1

10

9

8

7

6

5

4

3

2

1

7

6

5

4

3

2

1

Z1

10

9

8

7

6

5

4

3

2

1

7

6

5

4

3

2

1

0.7

frequency (GHz)

0.6

0.5

(S11(

0.7

frequency (GHz)

0.6

0.5

0.4

0.3

0.2

0.1

0

1.5

1.3

1.1

0.9

0.7

0.5

0.3

0.2

0.1

0

1.5

1.3

1.1

0.9

0.7

0.5

0.7

frequency (GHz)

0.6

0.5

0.4

0.3

0.2

0.1

0

1.5

1.3

1.1

0.9

0.7

0.5

0.7

frequency (GHz)

0.6

0.5

0.4

0.3

0.2

0.1

0

1.5

1.3

1.1

0.9

0.7

0.5

0.7

frequency (GHz)

0.6

0.5

0.4

0.3

0.2

0.1

0

1.5

1.3

1.1

0.9

0.7

0.5

0.7

frequency (GHz)

0.6

0.5

0.4

0.3

0.2

0.1

0

1.5

1.3

1.1

0.9

0.7

0.5

2.0

u1

1.6

1.2

0.8

0.4

0

2.0

1.6

1.2

0.8

0.4

0

2.0

u1

1.6

1.2

0.8

0.4

0

2.0

1.6

1.2

0.8

0.4

0

2.0

u1

1.6

1.2

0.8

0.4

0

2.0

1.6

1.2

0.8

0.4

0

two-point extraction

S

W2

L1

L2

W1

frequency (GHz)

(S21(

1.00

0.75

0.50

0.25

0

20

18

16

14

12

10

8

frequency (GHz)

(S21(

1.00

0.75

0.50

0.25

0

20

18

16

14

12

10

8

the given fine model response and the coarse

model response at

Q(x,V(i))

i

1.0

0.9

0.8

0.7

0.6

0.5

0.4

0.3

0.2

0.1

0

9

8

7

6

5

4

3

2

1

PE

PE

PE

(  (  (